## Slide 1: A Safer Defibrillator for Minimally Invasive Cardiac Surgery
Preliminary Oral Report
By Stephen Browning
Team Members: Kathleen Kafka and Kelly Moor

## Slide 2: Defibrillation Background
Fibrillation
  Uncoordinated and unpredictable contraction of the myocardium
  Understood Causes
    Re-entry [2]
    Hyperautomaticity [1]
Defibrillation
  Clinically: Fully stimulate myocardium  refractory periods stop fibrillation  sinus rhythm continues
  Four Theories: Critical mass, Upper Limit of Vulnerability, Progressive Depolarization, and Virtual Electrode [3]

## Slide 3: Defibrillation Background (cont.)
  Defibrillation Efficacy [3]
  Defibrillation Threshold (DFT) Algorithms
    Step-Down failure (70%)
    Step-Up success (30%)
    Iterative increment-decrement (50%)
  Clinically
    Patient specific DFT unattainable
    Risk factors indicate elevated DFT [3]
    Must add safety factor

## Slide 4: Defibrillation Techniques
Biphasic Waveform
  Current industry standard
  More effective than monophasic [3]
Energy Requirement
  External (~200-400 J) [4]
    Between Scapulae – Over Cardiac Apex
    Left Axillary – Right pectoral
  Internal (~10-40 J) [3]
    Endocardial
      RV apex and RA median wall
    Epicardical
      Trans-ventricular

## Slide 5: Surgical Background Picture Citation [9]
Mini Sternotomy
8-10 cm incision in upper sternum
Excellent visualization of aorta and right atrium
Right Mini-Thoracotomy
4-6 cm incision in 4th intercostal space
Excellent right atrium visualization
Right Atria
Aortas

## Slide 6: The Problem
Surgeons can encounter fibrillation events at most stages of a heart surgery
  Minimally invasive surgeries use external pads to deliver defibrillation shocks
Problem with this solution
  Energy required ~200-400J
    Skeletal muscle contraction
    Skin burns
Must move to internal defibrillation
  Allows for the use of much lower energies (~10-40 J)

## Slide 7: Project Scope
Devise a safer method for cardiac defibrillation during a surgical procedure through a mini-sternotomy or a right mini-thoracotomy
Deliverables
  Surgical Protocol
  CAD drawings of all mechanical components
  Circuit diagrams for all electrical components
  Material Analysis
  Manufacturing Analysis
  Computational design analysis
  Cost Analysis

## Slide 8: Existing Solutions and Problems Picture Citation [10]
Too Rigid
  Internal Defibrillator
  operable with one hand (7706876)
  Current PhysioControl Internal
  Adult Paddles (PhysioControl)
Unavailable Access Method
  Internally deployable defibrillator (4567900)
  Methodes of surgically implanting a defibrillator electrode (5618287)
Permanently Implanted
  Lead fixation means (8019437)

## Slide 9: Preliminary Electrical Analysis

## Slide 10: Design Requirements
Must be compatible with PhysioControl LIFEPAK 20e Defibrillator unit
The Device must support all energy settings up to 70 J
The Device must support 845 V and 33 A
Connection between electrodes and defibrillator unit must be 2.5-3 m
Electrodes must fit through smallest mini-thoracotomy incision (largest dimension <4cm)
Electrodes must safely navigate anatomical barriers to placement sites
Electrodes must not damage cardiac tissue

## Slide 11: Design Requirements (cont.)
Shock shall be deliverable no more than 20 seconds after recognition of a fibrillation event [5] [6]
Must withstand sterilization from one of the following [7]
  Steam autoclave, ethylene oxide, Sterrad, Steris System 1, or gamma sterilization
Deployment Specific
  Leave-In
    Wires should be easily maneuverable and occupy only 1% of the surgical opening
  Rapidly Deployable
    Safely deployable in the defined time metric
Must be safe for all physicians and OR staff

## Slide 12: Organization of Responsibility
Kathleen
  Design: Mechanical Engineering problems
  Research: Defibrillation Techniques
Kelly
  Design: Computer Science/Signal Processing problems
  Research: Surgical Procedures
Stephen
  Design: Electrical Engineering problems
  Research: Current Technologies/Patents

## Slide 13: Design Schedule
  October 3- Group brainstorm for design ideas
  October 5- Webpage due
  October 9- Finalize design ideas
  October 13- Complete analysis to choose a design
  October 16- Complete required analysis on chosen design
  October 23- Finish rough draft of progress report
  October 26- Progress Report due
  November 3- Complete specific details of chosen design
  November 10- Finalize details of analytic efforts needed for design
  November 17- Determine manufacturer of device
  November 20- Perform cost analysis for device
  November 30- Complete rough draft of final report
  December 7- Final Report due

## Slide 14: References
Dubin, Dale. Rapid Interpretation of EKG’s. Cover Inc. 2000.
Iaizzo, Paul A. Handbook of Cardiac Anatomy, Physiology, and Devices. Springer Science LLC. 2009.
Friedman, Paul A. and Hayes, David L. Cardiac Pacing, Defibrillation, and resynchronization: A Clinical Approach. Wiley-Blackwell. 2008
Bojar, Robert M. et.al. Use of Self-Adhesive External Defibrillator Pads for Complex Cardiac Surgical Procedures. Annals of Thoracic Surgery. 1988; 46:586-588.
Windecker, Stephan et.al. The Influence of Ventricular Fibrillation Duration on Defibrillation Efficacy Using Biphasic Waveforms in Humans. 1999.
Bardy, Gust H. et.al. A prospective, randomized evaluation of effect of ventricular fibrillation duration on defibrillation threshold in humans. 1988.
LEMO USA. Medical Sterilization Methods. http://www.lemo.com/download/imagesprod/P_series_whitepaper.pdf.
Resuscitation Central. Understanding Defibrillation Waveforms. http://www.resuscitationcentral.com/defibrillation/biphasic-waveform/.
Gardner, Timothy J. and Spray, Thomas L. Operative Cardiac Surgery. Oxford Press. 2004.
PhysioControl. LIFEPAK 20 Accessories. http://www.physio-control.com/uploadedFiles/products/defibrillators/product_data/accessories/LP20-20e_Accessories_3301326_A.pdf.

## Slide 15: Questions?